## Slide 1: Intro
We sought to model k in large rivers that are SWOT-observable
[Lamont & Scott 1970]
  Requires near-surface dissipation rate
    Infeasible to measure directly at global scale
    A common model (in rivers) is [Moog & Jirka 1999]
      Assumes that all depth-scale turbulent production eventually masks its way down the energy cascade and is dissipated and so just uses stream power to reflect ‘form drag/shear’ via meanders, bed forms, channel geometry, etc. rather than just from the bed (the model usually used in lentic waters)
      BUT, is not necessarily indicative of near-surface turbulence as it is calculated across the depth-scale
        This might contribute to why relations in rivers don’t scale to the ¼ power, i.e. [Wang et al. 2021; Ulseth eta al. 2019; Raymond et al. 2012]

## Slide 2
is scale-dependent: form-drag dissipation only effects k if it reaches the surface [Moog & Jirka 1999], which is more likely if the depth-scale is smaller (all else equal).
Put another way, an “inefficient channel” generates more form drag that more readily reaches the surface, therefore exerting a greater influence on than an efficient channel with the same flow
SO, we hypothesize that is a valid model when a river channel is so inefficient that near surface is largely from form drag. Maximal inefficiency happens when hydraulic radius and depth are nearly equivalent (Stream B)
Further, if this is true, then we likely don’t need the small-eddy model and can predict k directly using depth-scale turbulence (i.e. ) in inefficient rivers
River channel geometry influences form-drag production and dissipation

## Slide 3
Workflow
Calculate Rh/H ratios and use them as thresholds for channel efficiency
For each set of inefficient channels:
  Fit two models: and for parameters a, b, and
  Plot the b parameter and the r2 score for
At what (if at all) efficiency threshold does b approximate 0.25 and r2 is maximized??
Results
Theoretical model is recovered when channel inefficiency is greatest (b=0.28, r2: 0.68) panels a, c, d
We can produce an ~identical but more parsimonious model by scaling k directly with depth-scale turbulence () panel b