## Slide 1: Intro
We sought to model k in large rivers that are SWOT-observable
[Lamont & Scott 1970]
  Requires near-surface dissipation rate
    Infeasible to measure directly at global scale
    Another common model (in rivers) is [Moog & Jirka 1999]
      Depth-scale form-drag (i.e. meanders, bars, riverbanks, etc.) enhances turbulence production/dissipation relative to other aquatic systems. Meaning, that is a depth-scale dissipation term and is not necessarily reflective of the near-surface dissipation rate
        Stream power is over the entire depth, and we calculate this using reach-averaged velocity, not surface velocity
        This might contribute to why relations in rivers don’t scale to the ¼ power, i.e. [Wang et al. 2021; Ulseth eta al. 2019; Raymond et al. 2012]

## Slide 2
is scale-dependent: what is considered form-drag is relative to the depth, and form-drag dissipation only effects k if it reaches the surface [Moog & Jirka 1999], which is more likely if the depth-scale is smaller (all else held equal).
Put another way, an “inefficient channel” 1) generates more form drag [Chow 1959] and 2) form-drag turbulence more readily reaches the surface. So, should exert a greater influence on surface dissipation () than in an efficient channel with the same flow

## Slide 3
SO, I hypothesize that is a valid model when a river channel is so inefficient that near surface is largely from form drag (i.e. ).
Further, if this is true, then we likely don’t need the small-eddy model and can predict k directly using depth-scale turbulence (i.e. ) in inefficient rivers
Workflow
Calculate Rh/H ratios and use them as thresholds for channel inefficiency
For each set of inefficient channels:
  Fit two models: and for parameters a, b, and
  Plot the b parameter and the r2 for
At what (if at all) inefficiency threshold does b approximate 0.25 and r2 is maximized??
Rh/H is low
Rh/H is near 1

## Slide 4
Results
Theoretical model is recovered when channel inefficiency is greatest (b=0.28, r2: 0.68) panels a, c, d
We can produce an ~identical but more parsimonious model by scaling k directly with depth-scale turbulence () panel b

## Slide 5: What does this mean for SWOT?
Using Brinkerhoff et al (2019) dataset (n=171,553), I found that 95% of SWOT-observable river measurements had Rh within 5% of H
  This theoretical model for k () is therefore generally valid in SWOT-observable rivers and we can exploit this physical model to build a parsimonious BIKER algorithm with minimal unknowns